## Slide 1: Lecture 2: Physical and Data Link Layer (Computer Network)
Dr. Shashi Bhushan
Computer Network

## Slide 2: The OSI Model: Foundation of Network Communication
Dr. Shashi Bhushan
01
What is the OSI Model?
Developed by ISO (International Standards Organization).
A conceptual framework to understand network interactions.
Divides network functions into 7 layers.

## Slide 3: 7 – Layers of ‘OSI Model’
Dr. Shashi Bhushan
02
7 - Layers of the OSI Model (Top to Bottom):
Application – Interface for user interaction.
Presentation – Data translation, encryption, compression.
Session – Session management between systems.
Transport – Reliable data transfer (TCP/UDP).
Network – Routing and addressing (IP).
Data Link – Node-to-node error-free transmission.
Physical – Raw bit transmission over a physical medium.

## Slide 4: Responsibilities of Physical Layer
Dr. Shashi Bhushan
03
Layer 1 – Physical Layer:
Transmits raw bits over physical medium (0s and 1s)
Responsible for electrical/optical signals, voltages, pin layout
Defines connectors, cable types, and transmission rates
Examples: Ethernet cables, Fiber optics, Hubs, Repeaters

## Slide 5: Responsibilities of Data Link Layer
Dr. Shashi Bhushan
04
Layer 2 – Data Link Layer:
Ensures reliable point-to-point (node-to-node) delivery
Handles framing, addressing (MAC), and error detection
Controls access to shared media (via MAC protocols)
Examples: Ethernet, PPP, Frame Relay

## Slide 6: Responsibilities of Physical Layer and Data Link Layer [Both]
Dr. Shashi Bhushan
05
Layer 1 & 2 Interaction:
DLL packages data into frames
Physical layer converts frames into signals
Together, they ensure data is prepared for transmission across networks

## Slide 7: How Layer 1 and Layer 2 Work Together(a)
Dr. Shashi Bhushan
06
Data Encapsulation Overview:
Application data → Segmented by Transport Layer → Packets at Network Layer
At Data Link Layer: → Packet is encapsulated into a Frame → Frame = [Header | Payload | Trailer] → Header contains MAC address, control info
At Physical Layer: → Frame is converted into electrical, optical, or radio signals

## Slide 8: How Layer 1 and Layer 2 Work Together(b)
Dr. Shashi Bhushan
07
Transmission Flow:
Sender:
Receiver:
Example:
Ethernet Frame: MAC Header | IP Packet | FCS (CRC)
Bit stream (Layer 1) is interpreted and rebuilt as Frame at Layer 2
Data
Bits
Signal
Frame
Signal
Frame
Data
Bits

## Slide 9: Learning Objective(s)
Dr. Shashi Bhushan
08
Understand:
The roles and functions of the Physical and Data Link layers in the OSI model
Types of transmission media (wired and wireless)
Switching techniques: circuit, packet, and message switching
How framing is performed at the Data Link Layer
Analyse:
Error detection techniques: parity, checksum, CRC, and Hamming code
Flow control and MAC (Medium Access Control) protocols
How data travels through layers using encapsulation and decapsulation
Apply:
Use command-line tools (e.g., ping, tracert, netstat, get-mac) to analyse Layer 1/2 behaviour
Identify appropriate transmission mediums for network scenarios
Evaluate switching types based on use case
Activities:
CLI demos, matching tables, calculations, protocol simulations, case studies, MCQs

## Slide 10: Transmission Media – Introduction
Dr. Shashi Bhushan
09
Transmission Media – The Physical Path of Data
Ques. What is Transmission Media?
Ans: It is the physical pathway that carries communication signals from one device to another.
Categorized into: → Wired (Guided Media) → Wireless (Unguided Media)

## Slide 11: Transmission Media – Categories(a)
Dr. Shashi Bhushan
10
Guided (Wired) Media:
Uses tangible physical paths like cables
Examples: Twisted Pair, Coaxial Cable, Fiber Optic Cable
Unguided (Wireless) Media:
Uses air or space for signal transmission
Examples: Radio waves, Microwaves, Infrared, Satellite

## Slide 12: Transmission Media – Categories(b)
Dr. Shashi Bhushan
11
Importance in Physical Layer:
Determines speed, signal quality, range, and reliability
Critical for bandwidth planning and physical topology
Parameters Influenced by Media:
Bandwidth
Attenuation (signal loss)
Noise Immunity
Cost and ease of installation

## Slide 13: Twisted Pair Cable(a)
Dr. Shashi Bhushan
12
Ques. What Is Twisted Payer Cable?
Ans. A type of guided medium consisting of pairs of insulated copper wires twisted together. Reduces electromagnetic interference (EMI) and crosstalk.
Types of Twisted Pair:
Unshielded Twisted Pair (UTP): a. Common in LANs; b. Cheaper, flexible, but more susceptible to noise
Shielded Twisted Pair (STP): a. Has metallic shielding; b. Better noise resistance, slightly more expensive

## Slide 14: Twisted Pair Cable(b)
Dr. Shashi Bhushan
13
Characteristics:
Bandwidth: Up to 10 Gbps (with Cat 6a/7)
Max length: ~100 meters (without signal degradation)
Easy to install and terminate
Use Cases:
Ethernet LANs (10BASE-T, 100BASE-TX, etc.)
Telephone networks

## Slide 15: Coaxial Cable(a)
Dr. Shashi Bhushan
14
Ques. What Is Coaxial Cable?
Ans. A guided transmission medium with a central copper conductor. It is Surrounded by an insulating layer, metallic shielding, and outer plastic jacket. It is Designed to protect signals from electromagnetic interference (EMI).
Structure Layers: a. Inner conductor (copper); b. Dielectric insulator; c. Metallic shield (braid or foil); d. Outer plastic cover

## Slide 16: Coaxial Cable(b)
Dr. Shashi Bhushan
15
Characteristics:
Higher noise immunity than twisted pair
Bandwidth: Up to several GHz
Supports Analog and digital signals
Longer distance support than UTP
Use Cases:
Cable TV distribution
Internet (broadband DOCSIS networks)
CCTV systems
Legacy Ethernet (10BASE2, 10BASE5)
Example:
RG-6 Coaxial Cable used in home broadband setups

## Slide 17: Fiber Optic Cable(a)
Dr. Shashi Bhushan
16
Ques. What Is Fiber Optic Cable?
Ans. A guided medium that transmits data as pulses of light through glass or plastic fibers. It Immune to electromagnetic interference (EMI). Also Ideal for long-distance, high-bandwidth communication.
Structure:
Core – Thin glass center where light travels
Cladding – Reflects light back into core
Buffer Coating – Protective outer layer

## Slide 18: Fiber Optic Cable(b)
Dr. Shashi Bhushan
17
Types of Fiber:
Single-Mode Fiber (SMF)
a. Thin core (~9 μm).
b. Long-distance transmission (up to 100 km+)
c. Used in telecom backbones
Multi-Mode Fiber (MMF)
  a. Thicker core (~50–62.5 μm)
  b. Shorter distances (~2 km)
  c. Used in LANs and campus networks

## Slide 19: Fiber Optic Cable(c)
Dr. Shashi Bhushan
18
Characteristics:
Bandwidth: 10 Gbps to 100 Gbps+
Range: 2 km (MMF) to 100 km+ (SMF)
Immune to EMI, secure, lightweight
More expensive and delicate than copper cables
Use Cases:
Internet backbone infrastructure
Data centers, ISPs, submarine cables
Example:
SMF used in a 5G cellular backhaul network
MMF in enterprise campus backbone

## Slide 20: Comparison of Transmission Media(s)
Dr. Shashi Bhushan
19
Feature | Twisted Pair (UTP/STP) | Coaxial Cable | Fiber Optic Cable
Medium Type | Copper Wires | Copper Core + Shield | Glass/Plastic Fiber
Transmission Speed | Up to 10 Gbps (Cat 6a/7) | Up to 1 Gbps+ | 10 Gbps to 100 Gbps+
Maximum Distance | ~100 meters | ~500 meters (without repeaters) | 2 km (MMF) – 100+ km (SMF)
EMI Resistance | Low to Moderate (better in STP) | High | Very High (Immune)
Cost | Low | Moderate | High
Flexibility & Installation | Easy | Moderate | Difficult
Use Cases | LANs, Telephony | Cable TV, CCTV, Broadband | Backbone, ISP, Data Centers

## Slide 21: Cost, Attenuation & Performance Factors
Dr. Shashi Bhushan
20
Q. What Influences Media Performance?
Cost: 1. Initial installation cost; 2. Maintenance and replacement; 3. Fiber is expensive; twisted pair is budget- friendly
Attenuation (Signal Loss): 1. Decrease in signal strength over distance; 2. Coaxial has less attenuation than twisted pair; 3. Fiber has the lowest attenuation (best for long range)
Bandwidth: 1. Max amount of data that can be transmitted per unit time; 2. Fiber offers highest bandwidth; 3. Twisted pair supports sufficient bandwidth for typical LANs
Noise Susceptibility: 1. Interference from external sources (EMI, crosstalk); 2. Shielded cables reduce noise (STP, coaxial); 3. Fiber is immune
Flexibility and Ease of Installation: 1. Twisted pair: easy to bend, terminate; 2. Coaxial: rigid but manageable; 3. Fiber: fragile and requires specialized tools
Example Scenario:
- A campus LAN with short distances = Twisted Pair (Cat6).
- Long-distance connection between cities = Single-mode Fiber

## Slide 22: Wireless Transmission Media – Overview
Dr. Shashi Bhushan
21
What Is Wireless Media?
Transmission of signals through air using electromagnetic waves
No physical conductor; relies on antennas and frequencies
Classified as unguided transmission
Key Features:
Mobility and flexibility
Ideal for difficult-to-wire environments
More prone to interference, weather, and security concerns

## Slide 23: Wireless Transmission Media – Types
Dr. Shashi Bhushan
22
Common Wireless Transmission Types:
Radio Waves
  Frequency: 3 kHz to 1 GHz
  Used in FM radio, mobile phones, Wi-Fi
Microwaves
  Frequency: 1 GHz to 300 GHz
  Used in satellite links, cellular networks, line-of-sight communication
Infrared (IR)
  Frequency: ~300 GHz to 400 THz
  Short-range communication: TV remotes, IR sensors

## Slide 24: Wireless Transmission Media - Use cases
Dr. Shashi Bhushan
23
Characteristics:
  Shared medium — subject to congestion and collisions
  Speed depends on frequency band and technology (e.g., Wi-Fi 6 = 9.6 Gbps theoretical max)
Example:
  Office wireless LAN using 802.11ax (Wi-Fi 6)
  Satellite Internet in rural locations using Ku-band microwave

## Slide 25: Radio Waves(a)
Dr. Shashi Bhushan
24
What Are Radio Waves?
  Electromagnetic signals with frequencies between 3 kHz and 1 GHzTransmit data through air in all directions (omnidirectional)Do not require line-of-sight between sender and receiver
Characteristics:
  Long wavelength; can pass through walls and buildings
  Suitable for both short and long-distance communication
  Low-frequency signals can diffract around obstacles (buildings, terrain)

## Slide 26: Radio Waves(b)
Dr. Shashi Bhushan
25
Applications:
  AM/FM Radio Broadcasting
  Television Broadcasting (analog/digital)
  Cordless Phones
  Wi-Fi (2.4 GHz band)
  Bluetooth (2.4 GHz)
Example:
A home Wi-Fi router using 2.4 GHz radio waves to cover multiple rooms

## Slide 27: Radio Waves(c)
Dr. Shashi Bhushan
26
Advantages:
  Wide area coverage.
  Penetrates non-metallic obstructions.
  Inexpensive deployment for low-power
  Communication.
  Limitations:
  Susceptible to interference and jamming.
  Limited security unless encryption is applied.
  Lower bandwidth compared to higher-frequency media.

## Slide 28: Microwaves(a)
Dr. Shashi Bhushan
27
What Are Microwaves?
  Electromagnetic waves with frequencies between 1 GHz and 300 GHz.
  Typically used in point-to-point wireless communication.
  Requires clear line-of-sight between transmitter and receiver.
  Characteristics:
  Shorter wavelength than radio waves.
  Cannot easily penetrate buildings or terrain.
  High directional focus = lower interference.

## Slide 29: Microwaves(b)
Dr. Shashi Bhushan
28
Applications:
  Satellite communication (uplink/downlink)
  Cellular networks (e.g., 4G LTE backhaul)
  Microwave links for long-distance backbone
  Wi-Fi 5 GHz and 6 GHz bands (part of microwave spectrum)
  Example:
  Microwave tower relays internet backbone signals between two cities.

## Slide 30: Microwaves(c)
Dr. Shashi Bhushan
29
Advantages:
  High bandwidth, suitable for high-speed data
  Focused beam limits signal leakage
  Used where fiber deployment is expensive or impractical
  Limitations:
  Weather-dependent (rain fade, fog impact)
  Requires alignment and clear path
  More expensive setup than radio wave solutions

## Slide 31: Infrared Transmission(a)
Dr. Shashi Bhushan
30
What Is Infrared?:
  Electromagnetic waves with frequencies just below visible light (~300 GHz to 400 THz)
  Used for very short-range, point-to-point communication.
  Requires line-of-sight; blocked by walls and obstacles
  Characteristics:
  Highly directional
  Low interference from nearby
  penetrate solid objects (walls, furniture)

## Slide 32: Infrared Transmission(b)
Dr. Shashi Bhushan
31
Applications:
  TV remote controls
  Wireless keyboards/mice
  IR data transfer between phones (legacy)
  Infrared sensors in automation systems
  Example:
  TV remote control using IR signals to send commands to the television

## Slide 33: Infrared Transmission(c)
Dr. Shashi Bhushan
32
Overview:
  Secure (confined beam, unlikely to be intercepted)
  Low power consumption
  No license required
  Limitations:
  Must be aligned properly (no obstacles)
  Limited range (typically < 5 meters)
  Affected by sunlight or ambient IR sources

## Slide 34: Modern Wireless Technologies(a)
Dr. Shashi Bhushan
33
Overview:
  These are common wireless technologies used in homes, businesses, and mobile networks. They vary in range, speed, and application.
  Wi-Fi (Wireless Fidelity):
  Based on IEEE 802.11 standards
  Operates in 2.4 GHz and 5 GHz bands (newer: 6 GHz with Wi-Fi 6E)
  Typical range: ~50 meters indoors
  Speed: Up to 9.6 Gbps (Wi-Fi 6)
  Use Case: Home/Office internet access, mobile connectivity

## Slide 35: Modern Wireless Technologies(b)
Dr. Shashi Bhushan
34
Bluetooth:
  Short-range wireless standard for personal devices
  Operates in 2.4 GHz ISM band
  Range: ~10 meters (Class 2); up to 100 meters (Class 1)
  Speed: ~2 Mbps (Bluetooth 5.0+ supports more)
  Use Case: Headphones, wearables, file transfer
  3. 5G (Fifth Generation Mobile Network):
  Operates across low (sub-1 GHz), mid (1–6 GHz), and high (mmWave: 24–100 GHz) bands
  Speed: 100 Mbps to 10 Gbps+
  Ultra-low latency (<1 ms)
  Use Case: Smart cities, IoT, autonomous vehicles, high-speed mobile internet

## Slide 36: Wireless Media – Security, Range & Performance
Dr. Shashi Bhushan
35
Feature | Radio Waves | Microwaves | Infrared | Wi-Fi | Bluetooth | 5G
Frequency | 3 kHz–1 GHz | 1–300 GHz | ~300 GHz–400 THz | 2.4 / 5 / 6 GHz | 2.4 GHz | <1 – 100 GHz
Range | Long | Medium–Long (LOS) | Very Short (LOS) | ~50 m | ~10–100 m | 100 m – km
Bandwidth | Low | High | Very Low | High | Low–Moderate | Very High
Interference | High | Medium | Low | High | Medium | Medium
Security | Low (open air) | Medium | High (line of sight) | Medium | High (pairing) | Medium–High (encrypted)
Application | Broadcasting | Satellite, Backhaul | Remotes, Sensors | LAN, Streaming | Wearables, Audio | IoT, Mobile, AR/VR

## Slide 37: CLI Activity – get-mac
Dr. Shashi Bhushan
36
Why Use CLI?
  Command-line tools help visualize real-time behavior and statistics at the lower layers of the OSI model
  Useful for analyzing physical connectivity, MAC addresses, and path tracing
  Commands Overview:
  Get-mac
  → Displays MAC (Media Access Control) addresses of local network interfaces
  → Helps identify the unique Data Link Layer address of each interface
  Example: get-mac
  Output: Physical Address Transport Name
  00-14-22-01-23-45 \Device\Tcpip_{...}

## Slide 38: CLI Activity – netstat -e, Tracert
Dr. Shashi Bhushan
37
netstat -e:
  Displays Ethernet statistics (bytes sent/received, errors)
  Useful for monitoring Physical and Data Link Layer performance
  Example: netstat –e
  Output: Bytes Received: 12345678
  Errors Received: 0
Tracert (Windows) / traceroute (Linux/Mac):
  Traces the path packets take to a remote host
  Identifies network hops; reflects behavior from Data Link to Network Layer
  Example: Tracert google.com

## Slide 39: Switching Techniques(a)
Dr. Shashi Bhushan
38
What Is Switching?
  A technique used in computer networks to direct data from source to destination efficiently.
  Determines how data flows through intermediate devices like switches, routers, and gateways.
  Operates at the Data Link and Network Layers, depending on the type.
  Why Is It Needed?:
  Allows multiple devices to share a communication medium.
  Reduces unnecessary traffic by sending data only where it's needed.
  Helps build scalable, efficient, and organized networks.

## Slide 40: Switching Techniques(b)
Dr. Shashi Bhushan
39
Key Switching Techniques (to be covered next):
  Circuit Switching – Pre-established dedicated path
  Packet Switching – Data split into packets, each routed individually
  Message Switching – Entire message stored and forwarded
Real-Life Analogy:
  Circuit Switching: Like a dedicated taxi ride — one uninterrupted trip
  Packet Switching: Like shipping packages via postal service — each takes its own route
  Message Switching: Like dropping off a full envelope at the post office — delayed delivery
Example Devices: a. Switches and hubs in LANs; b. Routers in WANs; c. Telephony switches in PSTN

## Slide 41: Circuit Switching(a)
Dr. Shashi Bhushan
40
What Is Circuit Switching?:
  A communication method where a dedicated physical path is established between sender and receiver before data transfer begins.
  All data follows the same fixed route during the entire session.
Key Characteristics::
  Path remains reserved and exclusive during transmission.
  Fixed bandwidth allocation.
  Common in traditional telephony networks (PSTN).
  Delays occur in setup phase, but data transfer is fast once the circuit is established.

## Slide 42: Circuit Switching(b)
Dr. Shashi Bhushan
41
Real-World Example::
  Landline telephone call: a path is set up when you dial, and it's held until you hang up.
  Advantages:
  Reliable and predictable connection.
  Minimal delay once connection is established.
  Suitable for real-time voice and video if path remains uninterrupted.

## Slide 43: Circuit Switching(c)
Dr. Shashi Bhushan
42
Disadvantages:
  Inefficient for bursty or idle data — resources are reserved even if not used.
  Poor scalability in data-heavy networks.
  Setup time introduces initial delay.
Where It's Used::
  Circuit-switched telephone networks.
  Legacy ISDN connections.
  Some private leased lines.

## Slide 44: Packet Switching(a)
Dr. Shashi Bhushan
43
What Is Packet Switching?:
  A data transmission method where messages are broken into small units called packets.
  Each packet is sent independently and may take different paths to the destination.
  Common in data networks like the Internet.
Key Characteristics:
  No dedicated path; shared resources across the network.
  Each packet contains a header with destination address.
  At the destination, packets are reassembled in correct order.

## Slide 45: Packet Switching(b)
Dr. Shashi Bhushan
44
Advantages:
  Highly efficient use of network resources.
  Supports multiple connections simultaneously.
  Scalable and fault-tolerant — packets can reroute around network issues.
Disadvantages:
  Packets may arrive out of order or get lost (requires retransmission).
  Needs sophisticated protocols to manage sequencing and reassembly.
  Variable latency and jitter (not ideal for real-time voice/video unless protocols like VoIP are used).

## Slide 46: Packet Switching(c)
Dr. Shashi Bhushan
45
Real-World Example::
  Sending a message via WhatsApp: Each message is broken into packets and sent across the internet; they may arrive out of order but are reassembled on the receiver’s end.
Where It’s Used::
  Internet (TCP/IP)
  Email, browsing, file downloads
  Voice over IP (VoIP), streaming (with buffering)

## Slide 47: Message Switching(a)
Dr. Shashi Bhushan
46
What Is Message Switching?:
  A switching technique where the entire message is sent from one node to another and temporarily stored at each intermediate node before forwarding.
  Each node waits to receive the full message before sending it to the next hop.
Key Characteristics::
  No dedicated path required.
  Messages are stored (buffered) and forwarded hop-by-hop.
  Each message includes destination address and routing information.

## Slide 48: Message Switching(b)
Dr. Shashi Bhushan
47
Advantages:
  Efficient use of network bandwidth.
  No need to pre-establish a path.
  Capable of handling message prioritization and routing.
Disadvantages:
  High delay due to buffering at intermediate nodes (not suitable for real-time communication).
  Requires large storage at each switch.
  Risk of message loss if storage is full or crashes.

## Slide 49: Message Switching(c)
Dr. Shashi Bhushan
48
Real-World Example:
  Email systems: full message stored on a mail server, then forwarded to the recipient's server.
Where It’s Used:
  Email systems
  Store-and-forward messaging in older networks
  Network queuing models for simulations

## Slide 50: Comparison of Switching Techniques
Dr. Shashi Bhushan
49
Feature | Circuit Switching | Packet Switching | Message Switching
Path Establishment | Required (before transfer) | Not required | Not required
Data Transfer Unit | Entire stream | Packets (small units) | Entire message
Store-and-Forward | No | Yes (per packet) | Yes (entire message at each node)
Delay Type | Setup delay only | Variable (per packet routing) | High (due to full-message storage)
Resource Utilization | Inefficient (fixed path) | Efficient (shared network paths) | Moderate
Ideal For | Real-time audio/video | Web browsing, file sharing, VoIP | Email-like systems
Example Use Case | Telephone networks (PSTN) | Internet (TCP/IP), WhatsApp, Zoom | Store-and-forward email systems

## Slide 51: CLI Example – Switching Behavior with ping and tracert
Dr. Shashi Bhushan
50
Tools
1. ping
Checks basic connectivity and round-trip time.
Example: ping google.com
Output: Reply from 142.250.193.174: bytes=32 time=28ms TTL=117
2. tracert (Windows) / traceroute (Linux/Mac)
Shows the path packets take (hops) across the network.
Example: tracert google.com
Output (excerpt):
        1 <1 ms 1 ms 1 ms 192.168.1.1
        2 18 ms 19 ms 20 ms ISP-Gateway
        3 25 ms 28 ms 26 ms core.router.example.net {…}
        10 42 ms 44 ms 43 ms google.com

## Slide 52: Transition to the Data Link Layer
Dr. Shashi Bhushan
51
Role of the Data Link Layer:
  Provides node-to-node data transfer.
  Handles framing, error detection/correction, and flow control.
  Interfaces directly with hardware through MAC (Media Access Control).
Real-World Analogy::
  If the Physical Layer is the raw electrical road, and switching is traffic direction,the Data Link Layer ensures the vehicle (data) is complete, intact, and has valid documentation (frame structure).

## Slide 53: Framing(a)
Dr. Shashi Bhushan
52
What Is Framing?
  Framing is the process of encapsulating data into structured units called frames before transmission.
  Frames include control information like addresses, error-check codes, and delimiters.
Why Is Framing Needed?
  Allows the receiver to distinguish individual data units.
  Enables detection of transmission errors.
  Helps manage flow and identify boundaries between messages.

## Slide 54: Structure of a Frame
Dr. Shashi Bhushan
53
Anatomy of a Data Frame:
  Header - Contains metadata and control information
  - Examples: Source & destination MAC addresses, frame type, length, priority flags
  Payload (Data) - The actual content to be delivered
  - Can be from the Network Layer or higher
  Trailer - Often used for error detection (e.g., CRC, checksum)
  - Helps identify corrupted or tampered frames

## Slide 55: Fixed vs Variable Length Framing(a)
Dr. Shashi Bhushan
54
Why Different Framing Methods?
  Different network protocols and environments require different methods for identifying the boundaries between frames.
  Two major approaches: Fixed Length and Variable Length.
1. Fixed-Length Framing::
  All frames are the same size.
  Receiver knows exactly where each frame starts and ends.
  Advantages: Simple to implement
  Fast parsing and minimal overhead
  Disadvantages: May waste bandwidth if the payload is smaller than the frame Not suitable for variable-size data
  Example: ATM (Asynchronous Transfer Mode)

## Slide 56: Fixed vs Variable Length Framing(b)
Dr. Shashi Bhushan
55
2. Variable-Length Framing::
  Frame length varies based on data size.
  Requires delimiters, headers, or length fields to detect boundaries.
  Advantages: Efficient use of bandwidth
  Ideal for dynamic traffic (e.g., web data, email)
  Disadvantages: Requires more complex logic for parsing
  Susceptible to framing errors if delimiters are corrupted
  Example: Ethernet, PPP (uses length field); HDLC (uses flag-based framing)

## Slide 57: Character-Oriented Framing(a)
Dr. Shashi Bhushan
56
What Is Character-Oriented Framing?
  A method of framing where special byte values (characters) are used to indicate the beginning and end of a frame.
  Often used in older text-based protocols (e.g., ASCII-based communication).
Frame Format Example::
| Start Flag (STX) | Payload | End Flag (ETX) |
  STX = Start of Text (usually ASCII 0x02)
  ETX = End of Text (usually ASCII 0x03)

## Slide 58: Character-Oriented Framing(b)
Dr. Shashi Bhushan
57
Key Concepts::
  Easy to implement when communicating in text-based formats.
  Used where control characters can be interpreted reliably.
Problem: Character Confusion:
  What if the data itself contains the same character as the delimiter (e.g., 0x02 or 0x03)?
  This would cause the receiver to misinterpret actual data as frame boundaries.
  Solution: Byte Stuffing
  Special characters in the data are preceded by an “escape” character (ESC, e.g., 0x1B).
  At the receiver end, ESC sequences are interpreted and restored to original data.

## Slide 59: Byte Stuffing – Escaping Control Characters
Dr. Shashi Bhushan
58
What Is Byte Stuffing?
  A technique used in character-oriented framing to prevent confusion between control characters (like frame delimiters) and data.
  Adds a special escape character (ESC) before any occurrence of control characters within the data.
Why It’s Needed::
  If the payload includes the same byte as the Start/End flag (e.g., STX = 0x02 or ETX = 0x03), the receiver may misinterpret it as a boundary.
  Stuffing ensures that delimiters are only interpreted as framing marks if not escaped.

## Slide 60: Bit-Oriented Framing(a)
Dr. Shashi Bhushan
59
What Is Bit-Oriented Framing?
  A framing technique that uses specific bit patterns (not bytes or characters) to mark the start and end of a frame.
  Offers better efficiency for transmitting binary data compared to character-oriented methods.
Frame Structure Example (HDLC)::
  | Flag | Address | Control | Payload | FCS | Flag |
  Flag: A unique 8-bit pattern used to denote frame boundaries (e.g., 01111110)

## Slide 61: Bit-Oriented Framing(b)
Dr. Shashi Bhushan
60
Why Use Bit-Oriented Framing?:
  Allows for data independence—any kind of binary data can be transmitted.
  Common in high-performance, low-level data link protocols.
Problem: Bit Pattern Collision:
  What if the data contains the same bit pattern as the flag (01111110)?
  The receiver might mistake it for a frame boundary.
Solution: Bit Stuffing:
  Insert a 0 after every five consecutive 1s in the data stream.
  This prevents the accidental creation of the flag pattern.
Example:
Original data: 01111110 → Data collision risk Stuffed data: 011111010 → Safe transmission Receiver removes extra 0s when detecting five 1s.

## Slide 62: Bit Stuffing – Preventing Flag Confusion in Bit-Oriented Framing
Dr. Shashi Bhushan
61
What Is Bit Stuffing?:
  A technique used in bit-oriented framing to prevent confusion between data and control flags.
  Ensures that the flag pattern (typically 01111110) does not appear in the payload.
How It Works::
  The sender inserts a 0 after every five consecutive 1s in the payload. The receiver removes the 0 after every five 1s during de-stuffing.
  Example: Flag: 01111110
  Payload before stuffing: 011111101010→ Risk: Receiver might mistake 01111110 as a boundary
  Stuffed Payload :0111110101010 → Safe: Only flag is interpreted as boundary
  Framed Data: Flag | Stuffed Payload | Flag01111110 0111110101010 01111110

## Slide 63: Header-Based Framing – Count Field Method
Dr. Shashi Bhushan
62
What Is Count-Based Framing?:
  A framing technique where the length of the frame (or data portion) is included as a field in the header.
  Allows the receiver to know exactly how many bytes to expect, removing the need for flags or delimiters.
Advantages:
  Simple to parse
  Efficient for fixed-format protocols
  No need for bit or byte stuffing
Disadvantages:
  If the length field is corrupted, the frame is misinterpreted
  No synchronization markers if data is misaligned
  Not ideal on noisy or lossy links

## Slide 64: Error Detection(a)
Dr. Shashi Bhushan
63
What Is Error Detection?
  A mechanism used in data communication to identify errors introduced during transmission.
  Helps ensure that the received data matches what was originally sent.
  Implemented at the Data Link Layer (and sometimes at higher layers too).
Types of Errors:
  Single-bit error – Only one bit is altered
  Burst error – A sequence of bits is altered (more common in real scenarios)

## Slide 65: Error Detection(b)
Dr. Shashi Bhushan
64
Importance in Networking:
  Helps prevent corrupted data from reaching applications
  Enables retransmission or correction mechanisms
  Improves reliability over noisy or shared channels
Basic Error Detection Techniques (Coming Up)::
  Parity Bits (Simple & 2D)
  Checksum
  Cyclic Redundancy Check (CRC)

## Slide 66: Parity Bit
Dr. Shashi Bhushan
65
What Is Parity?:
  Parity is a basic error detection technique where a single bit is added to a data unit to make the total number of 1s either even or odd.
  Used to detect single-bit errors during transmission.

## Slide 67: Parity Bit – Simple and Two-Dimensional
Dr. Shashi Bhushan
66
1. Simple (Single) Parity::
  Even Parity: Add 1 if total number of 1s is odd (to make it even)
  Odd Parity: Add 1 if total number of 1s is even (to make it odd)
  Example:
  Data: 1010001 → Number of 1s = 3 (odd)
  → Even Parity Bit = 1 → Transmit: 10100011
2. Two-Dimensional Parity::
  Data is arranged in rows and columns
  Row parity and column parity bits are added
  Can detect and often locate a single-bit error
  Example:
  Original Block:
  | 1 | 0 | 1 | → Row Parity: 0
  | 0 | 1 | 0 | → Row Parity: 1
  Column Parity: 1 1 1
  → If a single-bit flips, the intersecting row and column reveal the location

## Slide 68: Checksum Method – Concept and Example
Dr. Shashi Bhushan
67
What Is a Checksum?:
  A simple error detection method where:
  → All data units (often words or bytes) are added together.
  → The result is complemented (inverted) and sent along with the data.
  The receiver performs the same sum and compares its result with the transmitted checksum.
Example (8-bit checksum)::
  Sender:
  Data bytes: 11001010 + 10110101 = 1B7 (in hex)
  Truncate carry: B7 → Complement: 48
  Transmitted: [11001010] [10110101] [01001000] (Checksum)
  Receiver:
  Adds all three:
  11001010 + 10110101 + 01001000 = 1FF
  → Truncate carry: FF → Complement = 00 (all bits 0) → Valid

## Slide 69: Cyclic Redundancy Check (CRC) – Concept
Dr. Shashi Bhushan
68
What Is CRC?:
  A robust error detection method that treats data as a binary number (polynomial).
  The sender divides the data by a generator polynomial and appends the remainder (CRC bits) to the frame.
  The receiver performs the same division — if remainder = 0, no error is detected.
Key Concepts::
  CRC detects burst errors more effectively than parity or checksum.
  Common CRC generators:
  CRC-8, CRC-16, CRC-32 (used in Ethernet, ZIP files, etc.)

## Slide 70: Cyclic Redundancy Check (CRC)
Dr. Shashi Bhushan
69
RC Operation (High-Level Steps):
  Append (n−1) zeros to the data, where n = degree of generator polynomial.
  Divide the resulting bitstream by the generator polynomial using modulo-2 division (XOR).
  The remainder is the CRC — added to the original data.
  Receiver repeats the division:
  → If remainder = 0 → Data is valid
  → Else → Error detected
Notation Example::
  Data: 1101011011
  Generator (key): 10011 (degree = 4)
  → Append 0000 to data → Divide → Remainder = CRC (e.g., 1000)

## Slide 71: CRC Calculation – Step-by-Step Example
Dr. Shashi Bhushan
70
Example Setup::
  Data: 100100
  Generator (Key): 1101 (degree 3 → append 3 zeros)
  Step 1: Append (n−1) zeros to data
  → 100100 → becomes 100100000
  Step 2: Perform Modulo-2 Division (XOR):
  Divisor (key): 1101
  Dividend: 100100000
  Perform binary division using XOR:
  Start with leftmost bits equal in length to the key
  XOR the segment with key
  Bring down the next bit and repeat
  Step-by-step XOR:
  1001 (from data)⊕ 1101 (key)
  = 0100 → bring down next bit (0) → 100
  ⊕ 110 → …continue process
  Final Remainder (CRC): e.g., 101
  Step 3: Append CRC to data
  Transmitted Frame: 100100 + 101 = 100100101

## Slide 72: Comparison of Error Detection Methods
Dr. Shashi Bhushan
71
Feature / Method | Parity Bit | Checksum | CRC
Detection Ability | Detects single-bit | Detects many errors | Detects burst & complex errors
Correction Ability | No | No | No
Complexity | Very low | Low | Moderate
Overhead | 1 bit (simple parity) | 1 word | n bits (depends on polynomial)
Performance | Fast | Fast | Efficient & reliable
Real-World Use | RAM, serial links | TCP/UDP, IP headers | Ethernet, USB, file formats

## Slide 73: Hamming Code – Error Correction Concept
Dr. Shashi Bhushan
72
What Is Hamming Code?:
  A forward error correction technique that not only detects errors but also corrects single-bit errors.
  Introduced by Richard Hamming in 1950.
  Uses parity bits placed at specific positions in the data to compute error location.
Example Format (7-bit Hamming Code for 4-bit data)::
  P1 covers positions 1, 3, 5, 7
  P2 covers positions 2, 3, 6, 7
  P3 covers positions 4, 5, 6, 7
Position | 1 | 2 | 3 | 4 | 5 | 6 | 7
Bit Type | P1 | P2 | D1 | P3 | D2 | D3 | D4

## Slide 74: Calculating Redundant Bits for Hamming Code
Dr. Shashi Bhushan
73
Hamming Code Redundancy Rule::
  To determine how many parity (redundant) bits are required for a given number of data bits (m), use the inequality:
  2^r ≥ m + r + 1
  Where:
  r = number of redundant (parity) bits
  m = number of data bits
Example:
  Suppose m = 4 (we want to encode 4 data bits)
  → Find r such that:
  2^r ≥ 4 + r + 1
  Try r = 3:
  2^3 = 8 ≥ 4 + 3 + 1 = 8 → Valid
  → So, 3 redundant bits are needed for 4 data bits (total = 7-bit Hamming Code)
Data Bits (m) | Redundant Bits (r) | Total Bits (m + r)
4 | 3 | 7
7 | 4 | 11
11 | 4 | 15
26 | 5 | 31

## Slide 75: Hamming Code – Encoding Example
Dr. Shashi Bhushan
74
Example: Encode 4-bit data = 1011 using Hamming(7,4):
  Step 1: Determine Positions
  Total bits = 7 (4 data + 3 parity)
  Position layout (left to right):
  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
  | P1| P2| D1| P3| D2| D3| D4|
  → Place data bits:
  D1 = 1, D2 = 0, D3 = 1, D4 = 1
  → Initial frame:
  [ _ P1 _ P2 _ D1 _ P3 _ D2 _ D3 _ D4 ]
  = [ _ _ 1 _ 0 1 1 ]
  Step 2: Calculate Parity Bits
  P1 (positions 1,3,5,7) → bits: 1,0,1 → P1 = 0 (even parity)
  P2 (positions 2,3,6,7) → bits: 1,1,1 → P2 = 1
  P3 (positions 4,5,6,7) → bits: 0,1,1 → P3 = 0
  → Final Frame:[P1 P2 D1 P3 D2 D3 D4] = [0 1 1 0 0 1 1]
  Final Encoded Hamming(7,4) Code: 0 1 1 0 0 1 1

## Slide 76: Hamming Code – Decoding and Error Correction
Dr. Shashi Bhushan
75
Received Example::
  Assume transmitted Hamming(7,4) frame = 0110011
  Now suppose a 1-bit error occurs → Receiver gets: 0010011
  Step 1: Recalculate Parity Bits
  Bit positions:
  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
  | P1| P2| D1| P3| D2| D3| D4 |
  Recalculate each parity bit using its covered positions:
  P1 checks bits 1, 3, 5, 7 → 0,1,0,1 → 0 parity = Correct
  P2 checks bits 2, 3, 6, 7 → 0,1,1,1 → 1 parity = Correct
  P3 checks bits 4, 5, 6, 7 → 0,0,1,1 → 0 parity = Correct
  → All parity bits correct? No — in this case, one parity is incorrect
  → Let's try an example with a flipped bit at position 3: 0100011
  Step 2: Identify Error Position
  Assume parity check results:
  P1 incorrect (1)
  P2 correct (0)
  P3 incorrect (1)
  → Error position = Binary 101 = 5
  → Flip bit at position 5 to correct
  Step 3: Extract Data Bits
  From corrected frame:
  | D1 | D2 | D3 | D4 | = bits at positions 3, 5, 6, 7

## Slide 77: Burst Error Handling Overview
Dr. Shashi Bhushan
76
What Is a Burst Error?:
  A burst error occurs when two or more consecutive bits in a data unit are altered during transmission.
  More difficult to detect and correct than isolated single-bit errors.
Characteristics:
  Common in wireless and noisy environments.
  Often caused by interference, sudden power changes, or synchronization loss.
  Length of a burst = from the first corrupted bit to the last (not just the number of erroneous bits).

## Slide 78: Handling Burst Errors
Dr. Shashi Bhushan
77
Example:
  Original: 10011101
  Received: 10110111
  → Error from bit position 2 to 5 → Burst length = 4
  Strategies for Handling Burst Errors:
  Block-Based Coding:
  Data is grouped into blocks with additional check bits.
  Burst errors affect fewer blocks → easier to isolate.
  Interleaving:
  Rearranges data bits before transmission to spread out burst errors.
  Makes errors appear as random single-bit errors when de-interleaved.
  CRC:
  Excellent for detecting burst errors (length ≤ degree of polynomial).
  Used in Ethernet, storage devices.

## Slide 79: Error Detection vs Error Correction
Dr. Shashi Bhushan
78
Feature / Technique | Parity Bit | Checksum | CRC | Hamming Code
Type | Detection | Detection | Detection | Detection & Correction
Detects Single-Bit Errors | Yes | Yes | Yes | Yes
Detects Burst Errors | No (limited) | Moderate | Excellent | Limited
Corrects Errors | No | No | No | Yes (1-bit)
Complexity | Very Low | Low | Medium | Medium
Redundancy/Overhead | 1 bit | 1 word | Multiple bits | Multiple bits
Used In | RAM, Serial Links | IP, TCP/UDP | Ethernet, USB | Memory, Embedded

## Slide 80: Introduction to Flow Control
Dr. Shashi Bhushan
79
What Is Flow Control?
  A mechanism to manage the rate of data transmission between two devices.
  Ensures that a fast sender does not overwhelm a slower receiver.
Why It’s Important::
  Devices often operate at different speeds or capacities.
  Without flow control, data may be lost if the receiver’s buffer overflows.
  Flow control preserves data integrity and network efficiency.

## Slide 81: Flow Control(b)
Dr. Shashi Bhushan
80
Where It Occurs:
  Implemented at the Data Link Layer (local flow control)
  Also at the Transport Layer (e.g., TCP windowing)
Key Objectives:
  Prevent receiver buffer overflow
  Ensure efficient use of bandwidth
  Maintain synchronization between sender and receiver
Common Flow Control Strategies:
  Stop-and-Wait
  Sliding Window (to be discussed in upcoming slides)

## Slide 82: Stop-and-Wait Flow Control
Dr. Shashi Bhushan
81
What Is It?:
  A basic flow control technique where the sender transmits one frame and waits for an acknowledgment (ACK) before sending the next.
Process:
  Sender transmits a frame.
  Receiver receives and sends back an ACK.
  Only after receiving the ACK does the sender transmit the next frame.
Example:
  Sender: → Frame 1 → (wait) ← ACK 1 ←
  → Frame 2 → (wait) ← ACK 2 ←

## Slide 83: Sliding Window Protocol – Introduction
Dr. Shashi Bhushan
82
What Is Sliding Window Protocol?:
  A flow control mechanism that allows the sender to send multiple frames before requiring an acknowledgment.
  Uses a “window” to define how many unacknowledged frames can be in transit.
Why It’s Better Than Stop-and-Wait::
  Improves channel utilization
  Allows continuous data flow
  Reduces idle time at sender

## Slide 84: Sliding Window – Example
Dr. Shashi Bhushan
83
Example Setup::
  Window size = 4
  Sender wants to send frames numbered 0–7
  Initial sender window: 0, 1, 2, 3
  Receiver can accept frames in order and send ACKs
Transmission Flow:
  Step 1:Sender sends frames 0, 1, 2, 3→ No ACKs yet; window is full
  Step 2:Receiver receives frames and sends ACK 0, ACK 1
  Step 3:Sender receives ACK 0→ Window slides: now can send frame 4→ Sender window: 1, 2, 3, 4
  Step 4:ACK 1 arrives→ Window slides again: frame 5 now allowed→ Sender window: 2, 3, 4, 5
  … and so on

## Slide 85: Media Access Control (MAC)
Dr. Shashi Bhushan
84
What Is MAC?
  Media Access Control is the sublayer of the Data Link Layer responsible for regulating access to a shared communication medium.
  Ensures that multiple devices can communicate over the same channel without interference or data collision.
MAC in the OSI Model::
  Data Link Layer is divided into:
  Logical Link Control (LLC): Handles error checking and frame synchronization
  Media Access Control (MAC): Manages access to the medium and hardware addressing

## Slide 86: MAC Addressing – Format and Function
Dr. Shashi Bhushan
85
What Is a MAC Address?
  A unique hardware address assigned to each Network Interface Card (NIC)
  Also known as a physical address or hardware address
  Used to identify devices on the same local network
Format:
  48 bits (6 bytes) long
  Written in hexadecimal: 00:1A:2B:3C:4D:5E or 00-1A-2B-3C-4D-5E
  First 24 bits: Organizationally Unique Identifier (OUI) assigned to manufacturer
  Last 24 bits: Device-specific identifier (NIC serial number)
Example :
MAC Address: 00:14:22:01:23:45
  00:14:22 → Assigned to Dell
  01:23:45 → Unique device ID

## Slide 87: MAC vs IP:
Dr. Shashi Bhushan
86
Feature | MAC Address | IP Address
Layer | Data Link Layer | Network Layer
Permanence | Usually fixed | Can change (dynamic)
Scope | Local (LAN only) | Global (WAN/LAN)
Format | Hexadecimal | Dotted decimal (IPv4)

## Slide 88: Contention-Based MAC – Introduction to CSMA
Dr. Shashi Bhushan
87
What Is Contention-Based Access?:
  A method where multiple devices share the same communication channel and compete (contend) for access.
  No centralized control — devices must listen and coordinate access themselves.
Key Principle: Carrier Sense Multiple Access (CSMA):
  Carrier Sense: Device listens to the medium before transmitting.
  Multiple Access: Many devices use the same medium.
  Goal: Minimize collisions by sensing before sending.

## Slide 89: Introduction to CSMA(b)
Dr. Shashi Bhushan
88
Variants of CSMA::
  CSMA/CD (Collision Detection) – Used in wired Ethernet (legacy)
  CSMA/CA (Collision Avoidance) – Used in wireless LANs (Wi-Fi)
Basic CSMA Process: :
  Device checks if channel is idle (Carrier Sense)
  If idle → transmit
  If busy → wait, then retry after random backoff
Advantages:
    Efficient in light network traffic
    Decentralized, simple to implement
Disadvantages:
    Risk of collision in high traffic
    Performance degrades as number of devices increases

## Slide 90: CSMA/CD – Collision Detection in Wired Networks
Dr. Shashi Bhushan
89
What Is CSMA/CD?:
  Carrier Sense Multiple Access with Collision Detection
  A method used in wired Ethernet (especially 10BASE-T and 100BASE-T) to detect and recover from collisions when two devices transmit simultaneously.
How It Works::
  Carrier Sense:→ Device listens to the channel before sending.
  Transmit:→ If the channel is idle, transmission begins.
  Collision Detection:→ While transmitting, the device listens for voltage changes (collision).→ If detected → transmission stops immediately.
  Backoff:→ Both devices wait a random amount of time (exponential backoff).→ After delay, devices retry transmission.

## Slide 91: CSMA/CA – Collision Avoidance in Wireless Networks
Dr. Shashi Bhushan
90
What Is CSMA/CA?:
  Carrier Sense Multiple Access with Collision Avoidance
  Used in wireless LANs (Wi-Fi) to minimize the chance of collisions before they happen
Why Collision Avoidance?:
  Unlike wired Ethernet, wireless devices cannot always detect collisions (hidden node problem)
  So, instead of detecting collisions, Wi-Fi tries to avoid them
How CSMA/CA Works?
  Carrier Sense:→ Device listens to the wireless channel
  If idle:→ Waits a random backoff time (Contention Window)→ Sends a frame if channel remains idle
  Optional RTS/CTS (Request to Send / Clear to Send):Helps reserve the channel before actual data transmissionMinimizes collision risk from hidden nodes
  ACK:→ Receiver sends an acknowledgment if the frame is received successfully

## Slide 92: CSMA/CD vs CSMA/CA – Comparison
Dr. Shashi Bhushan
91
Feature | CSMA/CD (Collision Detection) | CSMA/CA (Collision Avoidance)
Used In | Wired Ethernet (legacy) | Wireless LAN (Wi-Fi – IEEE 802.11)
Collision Handling | Detects collision and stops transmission | Avoids collision before transmission
Sensing Method | Listens and transmits simultaneously | Listens before transmitting
ACK Required | No (frames assumed successful) | Yes (ACK required to confirm reception)
RTS/CTS Mechanism | Not used | Optional (helps avoid hidden node issue)
Efficiency in High Traffic | Lower due to frequent collisions | Higher due to collision avoidance
Physical Media | Coaxial cables, shared wires | Wireless radio waves
Modern Usage | Rare (replaced by full-duplex switches) | Widely used in Wi-Fi

## Slide 93: Controlled Access Methods – Polling & Token Passing
Dr. Shashi Bhushan
92
What Is Controlled Access?:
  Devices transmit only when permitted, avoiding collisions entirely.
  Common in environments requiring order, predictability, or centralized control.
Polling:
  A central controller sequentially asks each device if it has data to send.
  Efficient when few devices are active.
Token Passing::
  A token (special frame) circulates in the network.
  Only the device holding the token may transmit.
  After transmission, the token is passed to the next node.

## Slide 94: MAC Protocols – Comparison Table
Dr. Shashi Bhushan
93
Feature | CSMA/CD | CSMA/CA | Polling | Token Passing
Access Type | Contention | Contention | Controlled | Controlled
Medium Type | Wired (Ethernet legacy) | Wireless (Wi-Fi) | Wired (Industrial) | Ring/Bus Topologies
Collision Handling | Detects after transmit | Avoids before transmit | No collisions | No collisions
Fairness | Medium | Medium | High (controller decides) | High (token rotation)
Efficiency (load) | Degrades with traffic | Degrades with traffic | Efficient if low traffic | Efficient but token delay
Complexity | Low | Moderate (RTS/CTS, ACK) | Moderate (controller needed) | High (token mgmt needed)

## Slide 95: MAC Address Filtering & Table Management
Dr. Shashi Bhushan
94
MAC Address Filtering::
  Restricts network access based on MAC address.
  Common in Wi-Fi routers and enterprise switches.
MAC Table Example:
MAC Address | Port
00:11:22:AA:BB:01 | 1
00:11:22:AA:BB:02 | 2

## Slide 96: MAC Address Conflicts – Causes
Dr. Shashi Bhushan
95
What Is a MAC Conflict?
  Occurs when two devices on the same LAN have the same MAC address.
  Leads to unpredictable behavior — data may go to the wrong device or be dropped.
Common Causes::
  MAC spoofing (malicious or accidental)
  Cloning (e.g., two virtual machines with same MAC)
  Misconfigured devices (e.g., reused NIC images in VM deployments)
  Faulty firmware or duplicate factory assignments

## Slide 97: MAC Address Conflicts – Detection & Resolution
Dr. Shashi Bhushan
96
Detection & Resolution::
  Use arp -a (Windows) or ip neigh (Linux) to check IP–MAC bindings
  Use switch CLI (show mac address-table) to identify MAC collisions across ports
  Change MAC address on one of the conflicting devices (if spoofed)
  Check DHCP server logs for duplicate MACs
Symptoms:
  Intermittent connectivity
  ARP table inconsistencies
  Packets looping, dropped, or misrouted

## Slide 98: CLI Tools – Inspecting MAC and Layer 2 Information
Dr. Shashi Bhushan
97
Windows:
  ipconfig /all → Shows MAC address (Physical Address)
  arp -a → Lists IP-to-MAC mappings (ARP cache)
  getmac → Lists MAC addresses of local interfaces
Example (Windows)::
  ipconfig /all
  → Ethernet adapter:
  Physical Address . . . . . . . . : 00-11-22-AA-BB-CC
  arp –a
  → Internet Address Physical Address Type
  192.168.1.1 00-11-22-AA-BB-CC dynamic

## Slide 99: Wireshark Overview – Capturing MAC-Layer Frames
Dr. Shashi Bhushan
98
What Is Wireshark?:
  A free, open-source network protocol analyzer
  Captures and displays network traffic in real time
  Useful for inspecting Layer 2 (Data Link) headers including MAC addresses
What You Can Observe:
  Ethernet frame structure (Destination MAC, Source MAC, Type, Payload)
  ARP, STP, and MAC broadcast traffic
  Duplicate MAC addresses or spoofing attempts
  CSMA/CD retransmissions or dropped frames (in legacy or emulated setups)

## Slide 100: Wireshark Overview – Capturing MAC-Layer Frames
Dr. Shashi Bhushan
99
Basic Steps::
  Select correct network interface
  Start capture
  Filter for protocols (e.g., eth, arp, stp)
  Inspect Frame → Ethernet II → Source/Destination MACs
Example Filter::
  eth.addr == 00:11:22:AA:BB:CC
  Useful Filters:
  Arp
  eth.src == aa:bb:cc:11:22:33
  eth.dst == ff:ff:ff:ff:ff:ff (broadcast)

## Slide 101: Wired vs Wireless MAC Behavior – Ethernet vs Wi-Fi
Dr. Shashi Bhushan
100
Ethernet (Wired LAN)::
  Medium: Dedicated cable per device (switch-based)
  Access Control: CSMA/CD (obsolete in switched networks)
  Collision Domain: One per switch port
  Efficiency: High due to full-duplex
  MAC Frames: Ethernet II format (Destination MAC, Source MAC, Type, Payload, CRC)
Wi-Fi (Wireless LAN)::
  Medium: Shared radio frequency
  Access Control: CSMA/CA (Collision Avoidance)
  Collision Domain: All stations in range
  Efficiency: Variable, affected by interference and range
  MAC Frames: IEEE 802.11 format (includes Frame Control, Duration, Addr1–3)

## Slide 102: Physical Layer vs Data Link Layer
Dr. Shashi Bhushan
101
Feature / Task | Physical Layer (Layer 1) | Data Link Layer (Layer 2)
Unit of Data | Bit | Frame
Role | Transmit raw signals | Format & deliver frames
Key Function | Signal encoding, transmission | Framing, error detection, MAC addressing
Devices | Cables, hubs, repeaters | Switches, NICs, bridges
Media Type | Electrical, optical, wireless | N/A (relies on Layer 1)
Addressing | None | MAC address
Visibility in Wireshark | Signal-level: Not visible | Yes – frame headers are visible

## Slide 103: Frame Formats – Ethernet vs Wireless (802.11)
Dr. Shashi Bhushan
44
Field | Description
Preamble | Synchronization (7 bytes)
Start Frame Delimiter | Marks start of frame (1 byte)
Destination MAC | 6 bytes
Source MAC | 6 bytes
Type/Length | 2 bytes (protocol or size)
Data (Payload) | 46–1500 bytes
Frame Check Sequence | CRC (4 bytes)
Ethernet Frame (IEEE 802.3 – Ethernet II):

## Slide 104: Frame Formats – Ethernet vs Wireless (802.11)
Dr. Shashi Bhushan
44
Wi-Fi Frame (IEEE 802.11):
Field | Description
Frame Control | Type, subtype, control flags
Duration/ID | Time slot reservation
Address 1 (Receiver) | Destination MAC
Address 2 (Transmitter) | Source MAC
Address 3 (BSSID/AP) | Intermediate or AP MAC
Sequence Control | Frame numbering
Data | Payload
Frame Check Sequence | CRC (4 bytes)

## Slide 105: Thank You
Dr. Shashi Bhushan
44